IMAGE DATA FORMATS
Outline
RGB image format and representation
YUV image format and representation
Grayscale
Histograms

---
RGB COLOR SPACE
- It is the most common format of image representation.
- Each pixel is represented by three color channels: Red, Green, and Blue.
Typically stored in 3-channel matrices (CV_8UC3) where accessing is done through the data type cv::Vec3b.
Color intensity values are of type unsigned char (8-bit uchar) ranging from 0(darkest) to 255(brightest).

---
YUV COLOR SPACE
- Popularly used in video image representation.
- Color encoding system used in analog TV.
- Bandwidth efficiency, as the luminance value of each pixel is prioritized over color information.
- Sub-sampling into formats like YUV 444, YUV 422, YUV 420 etc.

---
Cntd...
- In a YUV image, each pixel has three components (Y, U, V)
- Y component represents the brightness information (grayscale image).
- U and V components represent the color information.
- Often stored in 3 channel matrices.

---
YUV 422
- Image format with two channels
- Each pixel contains y (intensity) value and either u(blue sensitivity) or v(red sensitivity) value
- Highly efficient for broadcasting as low bandwidth required.

---
YUV Example
Original BGR Image
Retrived the Y(Grayscale values) only in single channel matrix

---
YUV 422 Example
Original BGR Image
Converted to YUV422 and back to BGR for display

---
Thresholding
- Common Image Processing Technique for image segmentation and object detection
- Binary Thresholding.
- Adaptive Thresholding.

---
Binary Thresholding
- Simple threshold technique that converts an image into a binary image.
- A predefined threshold value is considered.
- If the pixel intensity is above the threshold, it is set to the maximum value (e.g., 255).
- If the pixel intensity is below the threshold, it is set to the minimum value (e.g., 0).

---
Adaptive Thresholding
- An extension of binary thresholding that dynamically determines the threshold value for each pixel
- Threshold value is based on the local image characteristics.
- Techniques:
  - Mean Adaptive thresholding.
  - Gaussian Adaptive thresholding.

---
Example: Binary Thresholding
From custom static binThreshold() function
From cv::threshold() function

---
Example: Adaptive Thresholding
From cv::adaptiveThreshold() function
From custom static adThreshold() function